## Slide 1: Firewalls

## Slide 2: Firewalls
Firewall must determine what to let in to internal network and/or what to let out
Access control for the network
Internet
Internal network
Firewall

## Slide 3: Firewall as Secretary
A firewall is like a secretary
To meet with an executive
oFirst contact the secretary
oSecretary decides if meeting is reasonable
oSecretary filters out many requests
You want to meet chair of CS department?
oSecretary does some filtering
You want to meet President of US?
oSecretary does lots of filtering!

## Slide 4: Firewall Terminology
Types of firewalls
oPacket filter  works at network layer oStateful packet filter  transport layer oApplication proxy  application layer oPersonal firewall  for single user, home network, etc.

## Slide 5: Packet Filter
Operates at network layer
Can filters based on
oSource IP address oDestination IP address oSource Port oDestination Port
oFlag bits (SYN, ACK, etc.)
oEgress or ingress
application
transport network link physical

## Slide 6: Packet Filter
Advantage
oSpeed
Less complicated
Disadvantages
oNo state
oCannot see TCP connections
oBlind to application data
application
transport network link
physical

## Slide 7: Packet Filter
Configured via Access Control Lists (ACLs)
oDifferent meaning of ACL than previously
Allow | Inside | Outside | Any | 80 | HTTP | Any
Allow | Outside | Inside | 80 | > 1023 | HTTP | ACK
Deny | All | All | All | All | All | All
Action
Source IP
Dest Source IP Port
Dest Port
Protocol
Intention is to restrict incoming packets to Web responses
Flag
Bits

## Slide 8: TCP ACK Scan
Attacker sends packet with ACK bit set,
without prior 3-way handshake
Violates TCP/IP protocol
ACK packet pass thru packet filter firewall
oAppears to be part of an ongoing connection
RST sent by recipient of such packet
Attacker scans for open ports thru firewall

## Slide 9: TCP ACK Scan
Packet Filter
Trudy
Internal
Network
ACK dest port 1207
ACK dest port 1208
ACK dest port 1209
RST
Attacker knows port 1209 open thru firewall
A stateful packet filter can prevent this (next)
oSince ACK scans not part of established connections

## Slide 10: Stateful Packet Filter
Adds state to packet filter
Operates at transport layer
Remembers TCP connections and flag bits
Can even remember UDP
packets (e.g., DNS requests)
application
transport network link
physical

## Slide 11: Stateful Packet Filter
Advantages
oCan do everything a packet filter can do plus...
oKeep track of ongoing
connections
Disadvantages
oCannot see application data
oSlower than packet filtering
application
transport network link
physical

## Slide 12: Application Proxy
A proxy is something that acts on your behalf
Application proxy looks at incoming application data
Verifies that data is safe
before letting it in
application
transport network link
physical

## Slide 13: Application Proxy
Advantages
oComplete view of connections and applications data
oFilter bad data at application
layer (viruses, Word macros)
Disadvantage
oSpeed
application
transport network link
physical

## Slide 14: Application Proxy
Creates a new packet before sending it thru to internal network
Attacker must talk to proxy and convince it to forward message
Proxy has complete view of connection
Prevents some attacks stateful packet filter cannot

## Slide 15: Firewalk
Tool to scan for open ports thru firewall
Known: IP address of firewall and IP address of one system inside firewall
oTTL set to 1 more than number of hops to
firewall and set destination port to N
oIf firewall does not let thru data on port N, no
response
oIf firewall allows data on port N thru firewall, get time exceeded error message

## Slide 16: Firewalk and Proxy Firewall
Trudy
Packet
filter
Router
Dest port 12343, TTL=4 Dest port 12344, TTL=4 Dest port 12345, TTL=4 Time exceeded
This will not work thru an application proxy
The proxy creates a new packet, destroys old TTL
Router
Router
Part 2  Access Control
Mark Stamp’s Information Security: Principles and Practices by Mark Stamp/ Deven Shah.
Copyright  2009 Wiley India Pvt. Ltd. All rights reserved.

## Slide 17: Personal Firewall
To protect one user or home network
Can use any of the methods
oPacket filter oStateful packet filter oApplication proxy